## Slide 1: Solar Phuket Energy Saving Calculation
Source: Profilesolar.com Phuket averages 5.8 kWh net energy per day per kW of installed capacity
15.4 kW installed x 5.8 = 89 kWh average energy per day
PEA rate with taxes/ fees = 4.9 baht per unit 08/24
89kWh x 4.9 B/ kWh = 437 B per day average energy value from solar
437 B per day x 365 = 159,542 B per year
System cost: 280,000/ 159,542 saving per year
= 1.7 year payback = 20 months
= 57% annual ROI
This analysis credits zero value for…
Increased shading under array= passive AC consumption reduction
Increase in property value
Future PEA tariff increases (+11% 09/24)
Marketing value of Eco/ Carbon Neutral property
https://profilesolar.com/locations/Thailand/Phuket/

## Slide 2: Lifetime savings (30 years)
Assumptions
1% array degradation per year (warranty)
Annual cleaning cost + new inverter year 10
PEA will keep rates unchanged (unlikely)
Chart: 15kW PV grid tie system Paradise Zum
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Cost | 279980 | 279980 | 293980 | 307980 | 321980 | 335980 | 349980 | 363980 | 377980 | 391980 | 465980 | 479980 | 493980 | 507980 | 521980 | 535980 | 549980 | 563980 | 577980 | 591980 | 665980 | 679980 | 693980 | 707980 | 721980 | 735980 | 749980 | 763980 | 777980 | 791980 | 805980
PEA savings | 0 | 159542 | 317488.58 | 473839.74 | 628595.48 | 781755.8 | 931725.28 | 1080099.34 | 1226877.98 | 1372061.2 | 1515649 | 1657641.38 | 1813992.54 | 1954389.5 | 2093191.04 | 2230397.16 | 2366007.86 | 2500023.14 | 2632443 | 2763267.44 | 2892496.46 | 3020130.06 | 3146168.24 | 3270611 | 3393458.34 | 3514710.26 | 3634366.76 | 3752427.84 | 3868893.5 | 3983763.74 | 4097038.56