## Slide 1: Solar Phuket Energy Saving Calculation
Source: Profilesolar.com Phuket averages 5.8 kWh net energy per day per kW of installed capacity
15.4 kW installed x 5.8 = 89 kWh average energy per day
PEA rate with taxes/ fees = 4.9 baht per unit 08/24
89kWh x 4.9 B/ kWh = 437 B per day average energy value from solar
437 B per day x 365 = 159,542 B per year
System cost: 280,000/ 159,542 saving per year
= 1.7 year payback = 20 months
= 57% annual ROI
This analysis credits zero value for…
Increased shading under array= passive AC consumption reduction
Increase in property value
Future PEA tariff increases (+11% 09/24)
Marketing value of Eco/ Carbon Neutral property
https://profilesolar.com/locations/Thailand/Phuket/

## Slide 2: Lifetime savings (30 years)
Assumptions
1% array degradation per year (warranty)
Annual cleaning cost + new inverter year 10
PEA will keep rates unchanged (unlikely)
Chart: 15kW PV grid tie system Paradise Zum
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Cost | 279980 | 279980 | 293980 | 307980 | 321980 | 335980 | 349980 | 363980 | 377980 | 391980 | 465980 | 479980 | 493980 | 507980 | 521980 | 535980 | 549980 | 563980 | 577980 | 591980 | 665980 | 679980 | 693980 | 707980 | 721980 | 735980 | 749980 | 763980 | 777980 | 791980 | 805980
PEA savings | 0 | 159542 | 317488.58 | 473839.74 | 628595.48 | 781755.8 | 931725.28 | 1080099.34 | 1226877.98 | 1372061.2 | 1515649 | 1657641.38 | 1813992.54 | 1954389.5 | 2093191.04 | 2230397.16 | 2366007.86 | 2500023.14 | 2632443 | 2763267.44 | 2892496.46 | 3020130.06 | 3146168.24 | 3270611 | 3393458.34 | 3514710.26 | 3634366.76 | 3752427.84 | 3868893.5 | 3983763.74 | 4097038.56

## Slide 3: Solar Phuket Energy Saving Calculation (+20% array)
Source: Profilesolar.com Phuket averages 5.8 kWh net energy per day per kW of installed capacity
17.6 kW installed x 5.8 = 102 kWh average energy per day
PEA rate with taxes/ fees = 4.9 baht per unit 08/24
89kWh x 4.9 B/ kWh = 500 B per day average energy value from solar
500 B per day x 365 = 182,570 B per year
System cost: 304,000/ 182,570 saving per year
= 1.66 year payback = 20 months
= 60% annual ROI
This analysis credits zero value for…
Increased shading under array= passive AC consumption reduction
Increase in property value
Future PEA tariff increases (+11% 09/24)
Marketing value of Eco/ Carbon Neutral property
https://profilesolar.com/locations/Thailand/Phuket/

## Slide 4: Lifetime savings (30 years)
Assumptions
1% array degradation per year (warranty)
Annual cleaning cost + new inverter year 10
PEA will keep rates unchanged (unlikely)
Chart: 17.6 kW PV grid tie system Paradise Zum
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Cost | 304000 | 304000 | 318000 | 332000 | 346000 | 360000 | 374000 | 388000 | 402000 | 416000 | 490000 | 504000 | 518000 | 532000 | 546000 | 560000 | 574000 | 588000 | 602000 | 616000 | 690000 | 704000 | 718000 | 732000 | 746000 | 760000 | 774000 | 788000 | 802000 | 816000 | 830000
PEA savings | 0 | 182570 | 363314.3 | 542232.9 | 719325.8 | 894593 | 1068034.5 | 1239650.3 | 1409440.4 | 1577404.8 | 1745369.2 | 1911507.9 | 2075820.9 | 2238308.2 | 2398969.8 | 2557805.7 | 2714815.9 | 2870000.4 | 3023359.2 | 3174892.3 | 3324599.7 | 3472481.4 | 3618537.4 | 3762767.7 | 3905172.3 | 4045751.2 | 4184504.4 | 4321431.9 | 4456533.7 | 4589809.8 | 4719434.5